## Slide 1
Short-wavelength lithography in semiconductor industry
Dr. Konstantin Tsigutkin, ASML Netherlands B.V.

## Slide 2: 1970s/80s: Geeks buy their first computers

## Slide 3: Today, it’s hard to imagine a world without chips
Notes: It is hard to imagine a world without semiconductor chips.
There would be no computers, for a start. No digital cameras, MP3 players, CDs, DVDs and games consoles. No mobile phones and no Internet. Not even a digital wristwatch.
Semiconductors can also be found in less obvious places. Cars contain dozens of chips: from the micro-controllers that regulate the engine to sensors that detect rain and turn on windshield wipers, a modern car is a computer on wheels.
Medical image scanners, household smoke detectors and even washing machines rely on chips.
There are few inventions that have transformed — and continue to transform — the world as dramatically as the invention of the silicon chip.
ASML makes the machines that are used to manufacture these chips. All of the world’s top chip makers are our customers, so chances are that every day, you use
a device that was partly made on our machines.
Photo credits:
http://www.flickr.com/photos/johanl/3044291684/
http://www.flickr.com/photos/mikelo/4126205344/
http://www.flickr.com/photos/johanl/4365558047/
http://www.flickr.com/photos/intelfreepress/6722296265/
http://www.flickr.com/photos/digitalshotgun/454380458/

## Slide 4: More than 180 billion chips are made every year
Data: WSTS
In 2012, 185 billion chips were produced — 27 for every man, woman and child on the planet.
This equals total sales of $238 billion.
Chart: 
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
Total IC units | 31.958 | 33.054 | 33.0729 | 37.7019 | 40.573 | 47.0753 | 47.8916 | 58.3332 | 58.7161 | 68.1191 | 86.5146 | 68.546 | 78.5557 | 90.29 | 105.1872 | 116.3485 | 137.3627 | 151.0998 | 155.2919 | 144.6317 | 186.3977 | 186.7726 | 184.8438
Notes: Note: 2012 data will be available early March

## Slide 5: Driving the semiconductor industry: Moore’s Law
Gordon Moore (1965): Number of transistors per chip doubles every year.
Later adjusted to two years, the trend has held for five decades.
Source: Intel Museum
Notes: But before we go into details, let’s take a step back, and look at the big overarching trend that has driven the semiconductor industry for the past decades.
In 1965, Gordon Moore, who later went on to be one of the co-founders of Intel, observed that the number of chips that could be inexpensively placed on a chip doubled every year as manufacturing technology advanced. He believed that trend would continue.
He later adjusted the period to two years, but the trend has held steady since.
Intel’s 4004 processor, launched in 1971, had 2,300 transistors. Today’s chips have more than a billion.
But chips have not gotten (much) larger. The transistors have gotten smaller.

## Slide 6: Key to Moore’s Law: Making smaller transistors
The first integrated circuit on silicon, on a wafer the size of a fingernail (Fairchild Semiconductor, 1959)
Today: More than a billion transistors on the same area (Intel, 2012)
Transistor length has shrunk by a million
Notes: Chips have not gotten (much) larger. The transistors have gotten smaller. Much smaller.
The first integrated circuit on silicon, the forefather of current chips, was made on a wafer the size of a fingernail.
With today’s manufacturing technology, we can fit more than a billion transistors onto the same area.

## Slide 7: Moore’s Law makes chips cheaper…
Source: Gartner. High quality Flash
Lithography cost per unit of memory $/GByte
10000
100
10
1
1000
$1,162 for 1 GB
$0.17 for 1 GB
Solid state hard drives
Smartphones
Notes: 7
7

## Slide 8: … and more energy-efficient Computations per Kilowatt hour double every 1.5 years
Source: Jonathan Koomey, Lawrence Berkeley National Laboratory and Stanford University, 2009
Dell Optiplex GXI
486/25 and 486/33 Desktops
IBM PC-AT
IBM PC-XT
Commodore 64
DEC PDP-11/20
Cray 1 supercomputer
IBM PC
SDS 920
Univac I
Eniac
EDVAC
Univac II
Univac III (transistors)
Regression results:
N = 76
Adjusted R-squared = 0.983
Comps/kWh = exp(0.440243 x year – 849.259)
Average doubling time (1946 to 2009) = 1.57 years
IBM PS/2E + Sun SS1000
Gateway P3. 733 MHz
Dell Dimension 2400
SiCortex SC5832
2008 + 2009 laptops
1.E+16
1.E+15
1.E+14
1.E+13
1.E+12
1.E+11
1.E+10
1.E+09
1.E+08
1.E+07
1.E+06
1.E+05
1.E+04
1.E+03
1.E+02
1.E+01
1.E+00
Computations per kWh
1940
1950
1960
1970
1980
1990
2000
2010
Notes: 8

## Slide 9: Moore’s Law means doing more with less
Cray 1: The first supercomputer
  8 megabytes of memory
  Weight of an elephant (5.5 tons)
  150 kilowatt power supply (enough for 50 households)
  Freon cooling system
  $8.8 million ($30 million in today’s dollars)
1976
Notes: 9
The year is 1976. At Los Alamos National Laboratories in the United States, the first “supercomputer” is installed. The Cray-1 weighs in at 5-1/2 tons, it comes with 8 megabytes of memory, a 150 kilowatt power supply and an “innovative Freon cooling system”. It set you back almost 9 million dollars – or 30 million dollars today adjusted for inflation. Today… (next slide)

## Slide 10: Moore’s Law means doing more with less
1976
2013
The supercomputer in your pocket:
a fraction of the
materials,
price,
power consumption
Notes: 10
…today we carry that sort of computing power in our pockets. The mobile phone is a supercomputer in your pocket: it completely wipes the floor with the Cray-1 in terms of performance (512 MB of memory – plus gigabytes and gigabytes of flash storage) and it does so at a fraction of the weight, materials, price, and power consumption. The processor in there probably doesn’t use much more than 1 Watt. It doesn’t require an industrial-strength cooling system, and it costs much less than $30 million.
This is what shrink means: doing more with less.
ASML has made a major contribution to shrink: our machines allow chip makers to pattern finer features, to shrink transistors, and to make chips more powerful and more energy-efficient at the same time.

## Slide 11: How semiconductors are made
Slicing
Polishing
Material deposition
or modification
Photoresist
coating
Exposure
Photo-lithography
Developing
and baking
Etching
Removing
the photoresist
(ashing)
Testing
Separation
(dicing)
Packaging
Mono-crystaline
silicon “boule”
(300 mm diameter
x ~1 m length)
Blank wafer
Completed
wafer
Chips
Module
Repeat for each layer
(chip is 3D structure
with 20-30 layers)

## Slide 12: Lithography is critical for shrinking transistors
Like a photo enlarger of old, lithography forms the image of chip patterns on a wafer
Notes: The critical technology for shrinking transistors is lithography.
What is lithography? If you’re old enough to remember how photos were printed on photo paper, you know how a lithography machine works.
We have a negative – we call it the mask, or the reticle – which contains the blueprint of the chip pattern.
Using intense laser light, this pattern is projected onto the wafer.
The wafer has earlier been coated with a light-sensitive substance, the photoresist.
When the unexposed parts are etched away, the pattern that we have projected is revealed.
In other words, lithography is the production step that creates the billions of transistors on a chip – their shape, their position, and the wires that connect them and create a working chip.

## Slide 13: The principle of Lithography
Rayleigh equation:
Notes: Lithography is the most critical part of the process to create these structures, whereby a pattern is imaged into the photoresist on the surface of a silicon wafer.
The smaller the feature size the higher the performance. Therefore there is a continuous demand to shrink the feature size.

## Slide 14: Rayleigh formula relations
CD = critical dimension/resolution (usually half-pitch of grating)
= wavelength (Hg i-line 365nm, KrF 248nm, ArF 193nm, EUV 13.5nm)
NA = numerical aperture of optics (immersion: NA > 1, “hyper-NA”)
k1 = factor for litho process “complexity”/”capability” (illumination settings, reticle, resist), minimum for single exposure = 0.25

## Slide 15
Immersion Lithography: High Numerical Aperture (NA)
Water improves resolution and depth of focus
Lens
Water
Lens
Air
38 nm features can be imaged with immersion scanners
Notes: Immersion lithography uses a liquid between the wafer and the lens to increase the depth-of-focus and resolution of the projected image (by increasing the numerical aperture (NA) of the lens). The primary advantage of immersion lithography is that it enables 193 nm wavelength scanners to image 38 nm features (and possibly below) in a single exposure.

## Slide 16: Optical advantage of immersion - Resolution
Replace the air between the projection lens and the wafer by a fluid (e.g. water) to increase the Numerical Aperture (NA)

## Slide 17
EUV = 13.5 nm radiation
Generated with a plasma source
Extreme Ultra Violet Lithography has 3 unique features
It requires atomic flat multilayer coated aspheric mirrors
and reflective masks
Measured shape accuracy: 45 pico meter
=> much less than the diameter of Si atom
CxHy = 1x10-9 mbar
H2O = 1x10-7 mbar
Design example
And all in vacuum system
Notes: Will talk to difference from what Pete presented.

## Slide 18: EUV has >35 years of history
USA:
40 nm hp
70nm
L&S
First publications on EUV (LLNL, Bell Labs, Japan)
ASML starts EUVL research program
Japan:
80
nm
160
nm
ASML ships first pre-production tool (Korea)
ASML ships 2 alpha tools: IMEC (Belgium) en CNSE (US)
40 nm hp
NL:
28 nm
Lines and spaces
40 nm hp
NL:
19 nm
Lines and spaces
’85
’91
’97
’00
’01
’06
’10
’86
’87
’84
’88
’89
’90
’92
’93
’94
’95
’96
NL:
5 mm
’98
’99
’02
’03
’04
’05
’07
’08
’09
’11
’12
Notes: 18

## Slide 19: Sources of soft X-ray radiation
Synchrotron radiation
Free Electron Lasers
X-ray tubes (e.g. Si L-edge at 100 eV)
High Harmonic Generation of fs-laser pulses
Plasma radiation sources
Plasma parameters
Source requirements for projection systems:
High EUV radiation power (average >100W)  High repetition rates for pulsed systems (>10 kHz)
High conversion efficiency (input energy  EUV)
Small emitting volume (< 1mm)
Long lifetime (1 year of continuous operation and longer)
Lab-size footprint
Reasonable cost of the equipment and operation

## Slide 21: EUV spectrum of Xenon plasmas
ne=1017-1019 cm-3
Te=10-30 eV

## Slide 22
Winner:
Tin!

## Slide 23: Laser-Produced Plasma vs Discharge-Produced Plasma
P
laser
EUV
Target
Plasma
Lens
Parameter |  | LPP | DPP
Pulse duration | ns | 0.2 – 10 | 10 – 100
Energy | J/Puls | 0.25 – 1.5 | 2 – 10
Diameter | mm | 50 – 100 | 100 – 500
Typical parameters for laser and discharge produced plasmas
Laser produced plasma
Discharge produced plasma
Te ~ 10 – 500 eV
ne ~ 1017 – 1021 cm-3

## Slide 24: Two EUV Sn-source concepts are in use

## Slide 25: LDP concept – Tin flow on fast rotating wheels
Very interesting thin film dynamics under the action of high centrifugal forces
Laser pulse to generate a cloud of Sn
Electrical spark for conversion into in-band EUV
Liquid metal for low resistive contact between plasma and capacitor bank
Regenerating liquid tin surface to avoid electrode erosion
Efficient heat removal by liquid metal cooling

## Slide 26: LPP source movie

## Slide 27: LPP Plasma generation principle

## Slide 28
Chip shrink will continue
Notes: 28

## Slide 29: Gas Discharge EUV sources for metrology applications

## Slide 30: Gas Discharge EUV sources for metrology applications

## Slide 31: Synchrotrons

## Slide 32: HHG fs-lasers
© Center for EUV Lithography, LASTI, University of Hyogo

## Slide 33: Nanotechnology
EUV
EUV