## Slide 1: XUV Lasers in Radiation Biology
Luděk Vyšín (vysin@fzu.cz)
Department of Radiation and Chemical Physics
Institute of Physics of the CAS
Na Slovance 2, 182 21 Praha 8
Department of Nuclear Chemistry, FNSPE of the CTU
Břehová 7, 115 19 Praha 1

## Slide 2: Outline
Introduction – motivation
Interaction of XUV and SXR with matter
Interaction of charged particles with matter
Experimental sources of XUV/SXR
Biological samples
Interaction of XUV/SXR with DNA
Dosimetry and Radiation chemical yield
Results
Future plans

## Slide 3: Introduction - motivation
Development of proton (ion) accelerators based on „short“ laser pulses (~ns) delivered to solid targets (Ti) for radiotherapy
Radiobiology of ultra-high dose rates UHDR (dD/dt > 109 Gy s-1)
Application of the soft X-ray (SXR) a extreme UV (XUV) radiation to simulate the interaction effects of charged particles traversing a tissue. The so called „spur overlap“ effect can be studied using such experimental sources
To compare the effects of conventional (monochromatic) radiation sources to the effects of the experimental ones
Apply the standard techniques to study the effects in UHDR on a molecular level. Can be useful in a future medical applications (ELI - Med)
Compact size of experimental sources allows experiments in ordinary laboratory environment

## Slide 4: Outline
Introduction – motivation
Interaction of XUV and SXR with matter
Interaction of charged particles with matter
Experimental sources of XUV/SXR
Biological samples
Interaction of XUV/SXR with DNA
Dosimetry and Radiation chemical yield
Results
Future plans

## Slide 5: Interaction of XUV and SXR with matter
Radiation very strongly absorbed. Dependent on elemental composition and density of the absorbing specie.
Attenuation length ~ 1 – 10 nm
Interaction exclusively due to the photoelectric
effect followed by Auger electrons emission (low Z)
H2O

## Slide 6: Charged particles vs. photons (gamma)
Penetration depth (dose–depth curve)
4 field stereotactic irradiation
Single field irradiation
photons
protons
photons
protons

## Slide 7: Laser Driven Proton Acceleration (LDPA)
Yogo, Jpn J ApplPhys 50 (2011)
γ-H2AX
staining antibody
A549 pulmonary adenocarcinoma

## Slide 8: Outline
Introduction – motivation
Interaction of XUV and SXR with matter
Interaction of charged particles with matter
Experimental sources of XUV/SXR
Biological samples
Interaction of XUV/SXR with DNA
Dosimetry and Radiation chemical yield
Results
Future plans

## Slide 9: Interaction of charged particles with matter
Spectrum may be viewed as a flux of photons with a range of energies with cutoff at:
Perpendicular component can be represented by its Fourier transform:
Soft collisions:

## Slide 10: Absorption of Energy in H2O and DNA
Absorption of energy from photons
Absorption of energy from fast charge particle
Energy loss function

## Slide 11: Track Structure of the Fast Charged Particle
Geant4 track simulation - 100 p+ in air (30 cm track length)
30 MeV
200 MeV
Effects of ionizations and excitations of high density at a timescale of nanoseconds can be simulated using XUV and SXR sources
Track core:
(excitations, ionizations)
Penumbra:
δ-electrons distance (ionizations)

## Slide 12: Outline
Introduction – motivation
Interaction of XUV and SXR with matter
Interaction of charged particles with matter
Experimental sources of XUV/SXR
Biological samples
Interaction of XUV/SXR with DNA
Dosimetry and Radiation chemical yield
Results
Future plans

## Slide 13: Experimental sources of XUV/SXR
Prague Asterix Laser System: Ar and Xe plasma emission (500 ps)
Ar
Xe

## Slide 14: Experimental sources of XUV/SXR
PALS (Prague Asterix Laser System) – SXR (250 – 1570 eV)
Xe/He plasma
Ar/He plasma
Gas puff target

## Slide 15: Experimental sources of XUV/SXR
PALS (Prague Asterix Laser System) – SXR (250 – 1570 eV)
Zn target – QSS (Ne-like zinc)
Wavelength: 21.2 nm (58.5 eV)

## Slide 16: Experimental sources of XUV/SXR
Ne-like Ar8+ capillary discharge laser (CDL)
Laser emission by Z-pinch effect of Ar8+ plasma (Pulsed source)
Laser transition between 1S0(2p1/23p1/2)J=0 a 1P1(2p1/23s1/2)J=1 states
S. Heinbuch et al.: Optics Express 13, 4050 (2006)
Extreme UV (XUV) capillary discharge laser (IOP CAS)

## Slide 17: Experimental sources of XUV/SXR
Extreme UV (XUV) capillary discharge laser (IOP CAS)
Output characteristics | 
Wavelength | 46.9 nm
Δλ/λ | 8x10-4
Pulse length | 2 ns (FWHM)
Pulse energy | 1 μJ
Rep. rate | 12 Hz (3 Hz)
XUV beam

## Slide 18: Experimental sources of XUV/SXR
Nd: YAG Laser: 1024 nm, 0.75 J, 4 ns, 10 Hz, rep. rate: 30 Hz
Ar plasma emission: 4.2 x 1014 photons/m2 per pulse at sample position (in vacuum chamber)
He cell:
Source of soft X-ray radiation in “water window “ energy range (WAT)

## Slide 19: Radiation sources
IOE - MUT: Ar plasma emission (5 ns)
D. Adjei et al.: Rad Phys Chem 120, 17 (2016)

## Slide 20: Outline
Introduction – motivation
Interaction of XUV and SXR with matter
Interaction of charged particles with matter
Experimental sources of XUV/SXR
Biological samples
Interaction of XUV/SXR with DNA
Dosimetry and Radiation chemical yield
Results
Future plans

## Slide 21: DNA Samples
21
AFM
Stabilized by TE buffer (Tris-HCl:EDTA in different ratios)
Dried in N2 atmosphere
Plasmid DNA: extracted circular nucleic acid molecule (4361 bp long) M = 2.86×106 Da
© Egor Ukraintsev, PhD
60Co gamma (1.25 MeV)

## Slide 22: Outline
Introduction – motivation
Interaction of XUV and SXR with matter
Interaction of charged particles with matter
Experimental sources of XUV/SXR
Biological samples
Interaction of XUV/SXR with DNA
Dosimetry and Radiation chemical yield
Results
Future plans

## Slide 23: Interaction of XUV/SXR with DNA
Plasmid DNA: direct vs. indirect effect
Adhikary A., Electron spin resonance of radicals in irradiated DNA. (2014)

## Slide 24: Interaction of XUV/SXR with DNA
Adhikary A., Electron spin resonance of radicals in irradiated DNA. (2014)
DNA damage pathway

## Slide 25: Absorption of DNA in electromagnetic spectrum
Optical constants:
π → π* excitation of heterocycles of bases (4.7 eV až ~6.5 eV): T-T (T-C) dimers in far UV (<8 eV)
σ – excitations connected with sugar-phosphate backbone (> 7.8 eV)
σ → σ* excitation of bases (13.8 eV)
dR + hv → dR• leads to SSBs and DSBs (the yield of DSBs rise with the secondary electrons energy)
Plasmid DNA: pBR322 (4361 bp)

## Slide 26: Interaction of XUV/SXR Radiation with DNA
Effects of XUV (46.9 nm) on plasmid DNA breakage demonstrated:
Nováková et al.: Phys. Rev. E 91 (4), 042718, 2015
SSB
DSB
SSB*

## Slide 27: Interaction of XUV/SXR Radiation with DNA
Effects of XUV (46.9 nm) on plasmid DNA demonstrated:
Nováková et al.: Phys. Rev. E 91 (4), 042718, 2015
C
S
L

## Slide 28: Interaction of XUV/SXR Radiation with DNA
Effects of XUV (46.9 nm) on plasmid DNA demonstrated:
Nováková et al.: Phys. Rev. E 91 (4), 042718, 2015
C
S
L

## Slide 29: Detection of Plasmid DNA Forms
Agarose electrophoresis + SybrGREEN I
βSSB
f
S0
βDSB
www.yourgenome.org

## Slide 30: Outline
Introduction – motivation
Interaction of XUV and SXR with matter
Interaction of charged particles with matter
Experimental sources of XUV/SXR
Biological samples
Interaction of XUV/SXR with DNA
Dosimetry and Radiation chemical yield
Results
Future plans

## Slide 31: Dose and radiation chemical yield
Kerma [Gy]:
energy fluence [J/m2]
mass energy transfer
coefficient [m2/kg]
Dose [Gy]:
surface density [kg/m2]
Radiation chemical yield: Radiation chemical yield G(X) is the ratio of
n(X) and ε, where n(X) is the mean amount of matter of a specified nature
X formed, destroyed or changed by transfer of a mean amount of energy
ε to matter. G(X) = n(X)/ε
_
_
_
[mol/J]

## Slide 32: SXR chemical dosimetry
Water radiolysis:

## Slide 33: SXR chemical dosimetry
Water radiolysis:
Courtesy of Václav Štěpán, PhD
Geant4:DNA simulation

## Slide 34: SXR chemical dosimetry
Established fluorescent dosimetry systems:

## Slide 35: SXR chemical dosimetry
Fricke dosimeter:
1 mM FeSO4, 1 mM NaCl, 0.8 N H2SO4
Fe2+
Fe3+
ferrous
ferric
Ionizing radiation interacting with water produces a range of ions, radicals and molecules:
H OH H2 H2O2 H+ OH- e-aq
Molecular oxygen is needed and is a limiting factor
The maximum absorbed dose that can be measured is about 400 Gy

## Slide 36: SXR chemical dosimetry
G(Fe3+) – Radiation chemical yield (molecules/100 eV)
?

## Slide 37: Outline
Introduction – motivation
Interaction of XUV and SXR with matter
Interaction of charged particles with matter
Experimental sources of XUV/SXR
Biological samples
Interaction of XUV/SXR with DNA
Dosimetry and Radiation chemical yield
Results
Future plans

## Slide 38: Results
Action cross sections for pulsed sources (500 ps – 5 ns) in comparison to synchrotron radiation

## Slide 39: Results
G values for pulsed sources (500 ps – 5 ns) in comparison to synchrotron radiation

## Slide 40: Outline
Introduction – motivation
Interaction of XUV and SXR with matter
Interaction of charged particles with matter
Experimental sources of XUV/SXR
Biological samples
Interaction of XUV/SXR with DNA
Dosimetry and Radiation chemical yield
Results
Future plans

## Slide 41: Future plans
Femtosecond XUV/SXR laser (laser-plasma) sources would be beneficial in the study of the dose rate effect
Wider range of XUV photon energies
Apply theoretical modelling approach (fs time scale)
Use of mass spectrometry to determine the fragmented species (damaged bases)
Use of restriction enzymes to distinguish between the damage localized on sugar-phosphate backbone (strand breaks) and nucleobases (abasic sites)

## Slide 42: Acknowledgements
Department of radiation and chemical physics IOP CAS
Tomáš Burian
Eva Nováková
Martin Přeček
Libor Juha
Department of personal dosimetry, INP CAS
Marie Davídková
Kateřina P. Brabcová
Václav Štěpán
Department of nuclear chemistry, FNSPE – CTU
Kateřina Tomanová
Martin Vlk
Václav Čuba
Viliam Múčka
Wojskowa Akademia Techniczna
Przemyslaw Wachulak
Andrzej Bartnik
Henryk Fiedorowicz
Daniel Adjei
Mesfin Getachew Ayele
PALS facility
Eduard Krouský
Miroslav Krůs
Thank you for your
attention